## Slide 1: Linear Block Codes part1
Contents:
Communication block diagram
Types of codes,
linear and systematic
Encoding
Hamming Distance, Hamming weight
Syndrome calculation, decoding, etc
Standard array
Shivani M Deosthale

## Slide 2
Change to an efficient representation, i.e., data compression.
Source
Channel
coder
Source
coder
Channel
Source
decoder
Sink,
receiver
Channel
decoder
Channel
Any source of information
Change to an efficient representation for, transmission, i.e., error control coding.
Recover from channel distortion.
Uncompress
The channel is anything transmitting or storing information – a radio link, a cable, a disk, a CD, a piece of paper, …

## Slide 3
Transmission through noisy channel
* Transmission errors can occur, 1’s become 0’s and 0’s become 1’s
* To correct the errors, some redundancy bits are added to the information sequence, at the receiver the correlation is exploited to locate transmission errors
* Here, only binary transmission is considered.
*Here we try to optimally add this redundancy to the information bits.
*Codes which allow only error detection are called error detecting codes and codes which allow error detection and correction are called error detecting and correcting codes

## Slide 4
A parity bit is used for the purpose of detecting errors during transmission of binary information. A parity bit is an extra bit included with a binary message to make the number of 1s either odd or even.
The message including the parity bit is transmitted and then checked at the receiving end for errors.
• An error is detected if the checked parity does not correspond with the one transmitted.
• The circuit that generates the parity bit in the transmitter is called a parity generator and the circuit that checks the parity in the receiver is called a parity checker.
• In even parity the added parity bit will make the total number of 1s an even amount. In odd parity the added parity bit will make the total number of 1s an odd amount.
• As a general rule in the digital system where the transmission system is relatively short, it may be assumed that probability of a single-bit error is small and that of a double-bit error and higher order errors is extremely small.

## Slide 5
Types of codes:
Block codes(n,k) , Convolutional codes
Convolutional codes(n,k,m): Here each encoded message block depends upon the corresponding k bit message block as well as on the previous m message blocks. Thus encoder has a memory order of m. This set of encoded sequences produced by a k-input, n-output encoder of memory of order m is known as (n,k,m) convolutional code.
Since it is memory based so is implemented with sequential logic circuit.
code rate = k/n , by keeping same code rate, redundancy can be added by increasing m
Block codes:
set of words having a well defined mathematical property, where each word is a sequence of a fixed number of bits.
K: message bits, n: number of coded bits , (n-k=r parity bits to be added to message bits to form coded bits)
Linear Block codes

## Slide 6
The encoder generates a block of n coded bits from k message bits and we shall call this as (n,k ) block code.
Linear block code: if a modulo 2 addition of two code words is also a valid code word then the block code is linear.
K bit message will have message words and n bit possible codewords will be .
Systematic codes:
*If in all the codewords we can find exactly the corresponding information sequence, the code is called systematic. It is convenient to group all these bits either at the end or at the beginning of the code word.
* In this case the generator matrix G can be divided into two sub
matrices [P | I ]. Or G matrix can be written as [ I | P]
[G ]kxn = [Pkx(n-k) | Ikxk] or [G ]kxn = [Ikxk |Pkx(n-k) ]
Where P is parity submatrix and I is identity submatrix. Identity submatrix places message bits in coded word systematically.

## Slide 7
Encoding steps:
Coded word [C]1xn = [D]1xk . [G ]kxn
[D] is a 1xk row vector of k bits message word.
As information is in binary, the operations are modulo 2, i.e, addition corresponds to EXOR operation whereas multiplication is AND operation.
e.g. [ 1 1 0] . 1 1 1
0 1 1
1 0 1 = [ 1.1 1.0 0.1 , 1.1 1.1 0.0, 1.1 1.1 0.1]
= [1 00 , 11 0 , 110 ]
= [ 1 , 0, 0]
Modulo 2 addition (EXOR) | Modulo 2 multiplication(AND)
00=0 | 0.0=0
01=1 | 0.1=0
10=1 | 1.0=0
11=0 | 1.1=1

## Slide 8
D1 D2 D3 D4
1 0 0 0 1 1 1
0 1 0 0 1 1 0
0 0 1 0 1 0 1
0 0 0 1 0 1 1
C
=
Example 1: Find code words.
Coded word [C]1xn = [D]1xk . [G ]kxn
[C1,C2,C3,C4,C5,C6,C7] = [ D1, D2, D3, D4, D1D2D3, D1D2D4, D1D3D4 ]
(2k ) = 24 Codewords
= 16 codewords
D1 | D2 | D3 | D4 | C1 | C2 | C3 | C4 | C5 | C6 | C7 | W(C)
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 4
0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 3
0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 4
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 2
0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 4
0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 4
0 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 3
1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 4
1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 3
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 3
1 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 4
1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 3
1 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 4
1 | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 4
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 7

## Slide 9
Associated with generator matrix G , there is another matrix with order ((n-k)xn) matrix , called as Hamming matrix denoted as H
[H](n-k)xn = [ [PT](n-k)xk | [I](n-k)x(n-k) ]
For [G] = 1 0 0 0 1 1 1 Find [H] = 1 1 1 0 1 0 0
0 1 0 0 1 1 0 1 1 0 1 0 1 0
0 0 1 0 1 0 1 1 0 1 1 0 0 1
0 0 0 1 0 1 1
I(kxk)
P(kx(n-k)
[PT](n-k)xk
[I(n-k),n-k)]

## Slide 10
Important Terms:
Hamming weight: Hamming weight of a binary n bit code word is defined as the number of non zero components i.e. number of ones and is denoted as w(c).
e.g. The Hamming weight of a codeword “0110011” is 4
The previous table has last column for Hamming weight of all valid code words for the given generator matrix.
Hamming Distance: It is the distance between the two code words C1 andC2 and is defined as the number of places in which they differ and is denoted as d(C1,C2)
e.g. if C1 is “ “ and
C2 is “ “
Then Hamming distance between them is d(C1, C2)= 4
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 0 | 1 | 0

## Slide 11
Hamming distance and Hamming weight
Property 1: d(C1, C2) + d(C2, C3) ≥ d(C1, C3) ……. (triangle inequality)
Property 2: d(v, w) = w(v + w)
Minimum distance of block code
dmin = min C1,C2 {d(C1,C2) : C1,C2∈ C and C1  C2}
If the code is linear: dmin = min{w(C1 + C2) : C1,C2∈ C and C1  C2}
= min{w(C3) : C3∈ C and C3  0}
= Wmin
Theorem: The minimum distance of a linear block code is equal to the minimum weight of its non zero code word.

## Slide 12
Example 2. For a (7,4) linear block code, the parity check matrix P is given by
[P] = 1 1 1
1 1 0
1 0 1
0 1 1
Find G matrix, H matrix.
Find all code words.
Find Hamming weight for all code words.
Find Minimum Hamming weight for this set of code words.

## Slide 13
Decoding
syndrome decoding: Consider (n,k) linear block code generated by generator matrix G and having corresponding Parity check matrix H. If C is the transmitted code word and r is the received code word at the received end of the noisy channel due to which r is different from C Transmitted.
C + e = r ; e is the error word or error vector.
Receiver is unaware of either C or e. Hence after receiving r, decoder must determine whether there is any error within r.
Calculation of Syndrome: S is called as Syndrome of r. if there is no error(i.e. e=0), then r=C (i.e. valid code word)and S=0. But in case of error , S0 as e 0
[S](1x(n-k)) = [r](1xn). [H]T(nx(n-k))
= [C+e]. [H]T
= C. [H]T + e. [H]T
= 0 + e. [H]T = e. [H]T
Channel
C
r
noise

## Slide 14
Example :3
So The syndrome is not a function of the transmitted codeword but a function of error pattern. So we can construct only a matrix of all possible error pattern with corresponding syndrome.

## Slide 15
Syndrome Table Construction
There are 2n possible received vectors.
There are 2k valid code words.
There are 2n-k possible syndromes
First we generate all the error patterns of length 1, and calculate the corresponding syndrome and put all of them into a matrix.
Then, we increase the error pattern weight and we do the same thing as before.
Each time if the new syndrome had already been saved, it will be thrown away and we continue with the next error pattern.
When all the 2k syndromes are found, the table is complete.
For the previous example (256,200) the size of the matrix is
256 = 7:2 1016, which is still too big.
Vahid Meghdadi

## Slide 16
*If the minimum distance of a block code C is dmin, any two distinct code vector of C differ in at least dmin places.
*A block code with minimum distance dmin is capable of detecting all the error pattern of dmin – 1 or fewer errors.
*However, it cannot detect all the error pattern of dmin errors because there exists at least one pair of code vectors that differ in dmin places and there is an error pattern of dmin errors that will carry one into the other.
*The random-error-detecting capability of a block code with minimum distance dmin is dmin – 1 ;
Number of errors can be detected = dmin – 1;
Error-Detecting Capabilities of a Block Code

## Slide 17
*An (n, k) linear code is capable of detecting 2n – 2k error patterns of length n.
*Among the 2n – 1 possible nonzero error patterns, there are 2k – 1 error patterns that are identical to the 2k– 1 nonzero code words.
If any of these 2k – 1 error patterns occurs, it alters the transmitted code word v into another code word w, thus w will be received and its syndrome is zero.
There are 2k – 1 undetectable error patterns.
If an error pattern is not identical to a nonzero code word, the received vector r will not be a code word and the syndrome will not be zero.
Number of errors can be corrected = (dmin -1)/2
For Example 3, find how many errors can be detected and corrected?
Error-Correcting Capabilities of a Block Code

## Slide 18
Error patterns for (7,4) linear block code.
Since n= 7 , and 1 bit error , number of patterns = 7C1 = 7  / (1  x 6 ) = 7
N=7, 2 bit error, number of patterns = 7C2 = 7 /(2  x 5 ) = (7 x 6 )/2 =21 and ……so on……
Single and double error patterns shown below.
The possible error combinations will be nCk = C(n,k)= n!(n−k)!×k!
e1 | e2 | e3 | e4 | e5 | e6 | e7
1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 1
e1 | e2 | e3 | e4 | e5 | e6 | e7
1 | 1 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 0 | 1 | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 1 | 0 | 0 | 0 | 0
---------------- |  |  |  |  |  | 
0 | 0 | 1 | 1 | 0 | 0 | 0
-------- |  |  |  |  |  | 
 |  |  |  |  | 1 | 1

## Slide 19
Standard Array and Syndrome Decoding
Let v1, v2, …, v2k be the code vector of C.
Any decoding scheme used at the receiver is a rule to partition the 2n possible received vectors into 2k disjoint subsets D1, D2, …, D2k such that the code vector vi is contained in the subset Di for 1 ≤ i ≤ 2k
Each subset Di is one-to-one correspondence to a code vector vi
If the received vector r is found in the subset Di , r is decoded into vi
Correct decoding is made if and only if the received vector r is in the subset Di that corresponds to the actual code vector transmitted
A method to partition the 2n possible received vectors into 2k disjoint subsets such that each subset contains one and only one code vector is described here
First, the 2k code vectors of C are placed in a row with the all-zero code vector v1 = (0, 0, …, 0) as the first (leftmost) element From the remaining 2n – 2k n-tuple, an n-tuple e2 is chosen and is placed under the zero vector v1
Now, we form a second row by adding e2 to each code vector vi in the first row and placing the sum e2 + vi under vi
An unused n-tuple e3 is chosen from the remaining n-tuples and is placed under e2.
Then a third row is formed by adding e3 to each code vector vi in the first row and placing e3 + vi under vi .
we continue this process until all the n-tuples are used.

## Slide 20
Standard Array

## Slide 21
D1 D2 D3 D4
1 0 0 0 1 1 1
0 1 0 0 1 1 0
0 0 1 0 1 0 1
0 0 0 1 0 1 1
C
=
Example4 : Find code words. Find syndrome table, standard array. Error detection and correction capability of a code.
Coded word [C]1xn = [D]1xk . [G ]kxn
[C1,C2,C3,C4,C5,C6,C7] = [ D1, D2, D3, D4, D1D2D3, D1D2D4, D1D3D4 ]
(2k ) = 24 Codewords
= 16 codewords
D1 | D2 | D3 | D4 | C1 | C2 | C3 | C4 | C5 | C6 | C7 | W(C)
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 4
0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 3
0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 4
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 2
0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 4
0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 4
0 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 3
1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 4
1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 3
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 3
1 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 4
1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 3
1 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 4
1 | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 4
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 7