## Slide 1
Topic 6: Addressing Modes of 8086
By: Mr. Binu Joy

## Slide 2: Why study addressing modes?
Addressing modes help us to understand the types of operands and the way they are accessed while executing an instruction.

## Slide 3: What are we going to study?
Addressing modes
  We will see the types of addressing modes present in 8086.
  We will study each addressing mode with example.

## Slide 4: Types of addressing mode in 8086
Immediate addressing mode
Direct addressing mode
Register addressing mode
Register Indirect addressing mode
Indexed addressing mode
Register relative addressing mode
Base plus index addressing mode
Base relative plus index addressing mode

## Slide 5: 1: Immediate addressing mode
In this type of mode, immediate data is part of instruction and appears in the form of successive byte or bytes
MOV AX,10ABH
AX
10 ABH

## Slide 6: 2: Direct addressing mode
In this type of addressing mode a 16-bit memory address is directly specified in the instruction as a part of it.
MOV AX,[5000H]
AX
Memory
5000
5001
5002
22
33
22
33

## Slide 7: 3: Register addressing mode
In this type of addressing mode, the data is stored in the register and it can be a 8-bit or 16-bit register. All the registers, except IP, may be used in this mode.
MOV AL,BLH
MOV AX,BXH
AH AL
AX
FF 33
BX
10 AB
BH BL
10 AB

## Slide 8: 4: Register Indirect addressing mode
The address of the memory location which contains data or operand is determined in a indirect way, using the offset register.
MOV AX,[BX]
Memory
5000
5001
5002
22
50 | 00
AX
BX
33
22
33

## Slide 9: 5: Indexed addressing mode
In this addressing mode, offset of the operand is stored in one of the index registers. DS is the default segment for index register SI and DI.
MOV AX,[SI]
Memory
5000
5001
5002
22
50 | 00
AX
SI
33
22
33

## Slide 10: 6: Register relative addressing mode
In this mode, the data is available at an effective address formed by adding an 8-bit or 16-bit displacement with the content of any one of the registers BX, BP, SI and DI in the default (either DS or ES) segment.
MOV AX, 50H[BX]
Memory
5051
5052
5053
44
50 | 00
AX
BX
33
Offset
+ 50H = 5050H
Final
Index
Address
44
33

## Slide 11: 7: Base plus index addressing mode
In this mode the effective address is formed by adding content of a base register (any one of BX or BP) to the content of an index register (SI or DI). Default segment register DS.
MOV AX, [BX] [SI]
3000
3001
3002
10 | 00
AX
BX
= 3000H
Final
Index
Address
20 | 00
SI
+
12
34
12
34

## Slide 12: 8: Base relative plus index addressing mode
In the effective address is formed by adding an 8 or 16-bit displacement with sum of contents of any one of the base registers (BX or BP) and any one of the index registers, in a default segment.
MOV AX,50H[BX][SI]
3050
3051
3052
10 | 00
AX
BX
= 3050H
Final
Index
Address
20 | 00
SI
12
50H +
34
12
34

## Slide 13
What we have learnt
  Different types of addressing modes present in 8086.
  Location of operands with respect to different addressing modes.
Summary

## Slide 14: References
Advanced Microprocessors and Peripheral
  - By K Bhurchandi, A. K. Ray

## Slide 15
This presentation is licensed to the public Text is available under the Creative Commons Attribution-ShareAlike License